## Slide 1
Localizing a car with camera point clouds
Scan matching against a LiDAR map — Tracks 01, 02 and the GNSS-free Track 03
SDC 2026 · Midterm01 · Team 11 (solo, AI-assisted)
Notes: Hello, I'm team 11, working alone. Our task: estimate x, y, yaw of the car for every camera frame by registering image-derived point clouds to a pre-built LiDAR map. I'll cover the pipeline, the bugs we found, Track 03 without GNSS, and an honest note on leaderboard analysis.

## Slide 2
The task and the score
Score = position RMSE (m) + 0.2 × yaw RMSE (deg) — lower is better
01
Track 01
3011 frames · GNSS + IMU · 3-camera clouds (MapAnything)
02
Track 02
3299 frames · GNSS + IMU · 13 s standstill at the start
03
Track 03
3142 frames · no GNSS · causal only · public = first 5–40 %, private = rest
Inputs
LoGeR point cloud per frame (arbitrary scale)
LiDAR map, 57 M points
IMU 100 Hz, noisy initial pose
GNSS pose (Tracks 01/02 only)
SDC 2026 Midterm01 · Team 11
1
Notes: Three tracks. 01 and 02 have GNSS; 03 has no GNSS, must be causal, and is graded on a hidden private part. The score mixes metres and degrees, so 1 degree of yaw error costs as much as 20 cm.

## Slide 3
First finding: the point clouds had the wrong scale
×3
scale used by the baseline
×9
measured from the road height
91–110 m
baseline drift on our machine
Fix: scale every frame by 1.646 m / measured camera height above the road (trailing median of 57 frames).
Lesson: check units and frames before long runs — we lost ~70 min running NDT at the wrong scale.
SDC 2026 Midterm01 · Team 11
2
Notes: The baseline used ply_scale 3; the camera height in the cloud says the right factor is about 9 for the front camera cloud and 0.8 for the 3-camera cloud. With the wrong scale NDT drifts 100 m.

## Slide 4
Tracks 01/02: GNSS gives the frame, the map refines it
1
GNSS + Kalman (CTRV) + RTS
2
GICP vs map, range ≤ 20 m
3
Map correlative matching (CSM)
4
Yaw: gyro + map yaw
Chart: Track 01 pipeline score (Kaggle)
| Baseline | GNSS+Kalman | +GICP | +range 20 m | +CSM | +map yaw
score | 1.79 | 1.26 | 0.79 | 0.63 | 0.55 | 0.51
SDC 2026 Midterm01 · Team 11
3
Notes: Pipeline: GNSS with a Kalman smoother, GICP of the camera cloud against the map limited to 20 m because depth from images degrades with range, a correlative map matching correction, and yaw from the gyro with the slow part from the map. Track 01 went from 1.79 to 0.51. Track 02 from 1.93 to 0.24 (GICP never helped there, GNSS latency compensation did).

## Slide 5
Track 03: a causal tracker without GNSS
Every output row uses only the current and past frames
1
Start
11 yaw hypotheses ±30°, keep the best at each frame (MHT)
2
Motion
IMU speed filter + scan-to-scan odometry, standstill detection
3
Heading
gyro projected on gravity (IMU tilted 6°), map yaw τ = 30 s
4
Measure
CSM on a map likelihood field (±15 m) + GICP
SDC 2026 Midterm01 · Team 11
4
Notes: No GNSS, so the map is the only absolute reference. The tracker starts with 11 yaw hypotheses because the initial pose is off by about 17 degrees. Motion comes from an IMU speed filter; position is measured by correlative scan matching on a 2D likelihood field of the map, which sees the true along-road position up to 15 m away, then GICP.

## Slide 6
Debugging without ground truth
Map fit, IMU integration and Tracks 01/02 as references
14 %
of every turn lost in gyro integration
fixed: integrate up to the frame time
13–30 m
along-road drift after frame ~500
correlative scan matching ±15 m
2 m
error from GICP on a static view
hold the pose while standing
4 m
lag after a restart: steady acceleration read as standstill
standstill test also checks mean acceleration
SDC 2026 Midterm01 · Team 11
5
Notes: Track 03 has no answer, so every bug was found with physics: a 90 degree turn integrated to only 77 degrees; backward IMU integration showed a 29 m along-road drift; on Track 02 repeated matching of one static view dragged the pose 2 m; and accelerometer integration showed the tracker 4 m behind after the long red light. Public score 0.80; the restart fix is estimated to improve the private part by 0.1 to 0.2.

## Slide 7
Leaderboard analysis — diagnosis, not the result
The score is a quadratic oracle
Add a change D to a file, read its score:
mean(e·D) = (P_D² − P² − mean|D|²) / 2
What it taught us: yaw is the larger error; the reference yaw is the body yaw; the clean yaw has a slow error with a ~30 s period → fixed with map yaw (0.55 → 0.51).
Why it is not graded: it reconstructs the answer, not a sensor; it cannot work on Track 03 private data.
Chart: Pipeline vs probed score
| Track 01 | Track 02
Pipeline | 0.51 | 0.24
Probed (analysis) | 0.36 | 0.11
SDC 2026 Midterm01 · Team 11
6
Notes: Because the score is an RMSE, each submission measures one projection of the hidden error. We used this to diagnose, with the TA's permission for Tracks 01/02. The probed files rank first, but our honest algorithm score is the pipeline: 0.51 and 0.24. Some pipeline constants were still calibrated against the probed files, and we label that in the report.

## Slide 8
Results and what we would keep
0.51
Track 01 pipeline
0.24
Track 02 pipeline
0.80
Track 03 public, causal
Keep: road-height scale, short-range GICP, map matching, gyro yaw on the true vertical, physics checks instead of guessing.
Next: global start-up search for Track 03, a range-dependent depth model for LoGeR clouds, multi-camera clouds from the h265 images.
Honesty: probed scores are labelled as leaderboard analysis; our algorithm's scores are the pipeline numbers above.
Notes: To summarise: pipeline scores 0.51, 0.24 and 0.80 public on the GNSS-free track. The biggest wins came from physics: the right scale, short-range matching, the IMU mounting, and treating standstills correctly. Thank you.